## Slide 1: People Counter using Thermal Tripwire Sensor
Team 8: Janis Intoy and Emily Lam
May 3rd, 2017

## Slide 2: Problem Statement
The efficiency of HVAC (Heating Ventilation & Air Conditioning) systems can be improved by making them adaptive to the number of people in a room.
In order to estimate a room’s occupancy level, the Occusense Senior Design team has created a thermal sensor system to capture the motion of people through doorways.
We develop a real- time algorithm to detect the direction of motion of people passing through in order to continuously track the number of people in the room.
Thermal Camera
Person Enter?
Person Exit?
Room Occupancy
Heating
Ventilation
Cooling
Notes: JANIS

## Slide 3: Assumptions and Constraints
Low frame rate (8-12 Hz) and low resolution 16x4 array thermal sensor
Low number of entry points
  Tripwire methodology
Background has slow temporal dynamics
Data starts with some number of background-only frames
Only vertical direction matters
IN
OUT
Notes: JANIS

## Slide 4: Implementation: Three-step Approach
Foreground Mask
3. Keep track of occupancy
Data
Background Subtraction
Algorithm
Foreground Mask
Optical Flow
Algorithm
Spatial Gradients
Classifier
People Count
Spatial Gradients Quiver
1. Detect a person in the doorway
2. Determine direction person is moving
Notes: EMILY

## Slide 5: Background Subtraction
Running Gaussian average
(with adaptive threshold)
background at each pixel
Foreground-adaptive
(McHugh et al., 2009)
Kernel density estimation of background and foreground models
<
Notes: JANIS

## Slide 6: Optical Flow
Gradient-based optical flow
Velocity can be modeled using spatially and temporal gradients
  Only vertical changes matter
A large v_y would correspond to a lot of motion in that direction
Due to boundary conditions, there are only 3x16 gradients
Direction Classifier
Spatial gradients are row-averaged and column averaged per a frame
Direction is computed based on the first and last frame of an event, comparing the gradients to obtain a direction
An event is defined as consecutive frames when motion is detected
Dynamic parameters for corner cases
Notes: EMILY

## Slide 7: Example: Walking out
Notes: JANIS

## Slide 8: Example: Lingering by the door
Notes: JANIS

## Slide 9: Example: Person running through door
Notes: EMILY

## Slide 10: Example: Multiple people together
Notes: EMILY

## Slide 11: Intermediate Results
o:
x--
-.
△-
(optical flow uses unmasked video)
o:
x--
-.
△-
Notes: JANIS

## Slide 12: Final Results: People Count
Notes: JANIS

## Slide 13: Conclusions and Future Work
90% accuracy
  Known issues:
    Foreground identification fails to detect person
    People walking in together
Challenges
  Optical flow with too much temporal changes in the middle frames of an event
  Distinguishing noise versus fast motion in single frame events
  Mean thresholding for determining the start and stop of events
Future Work
  Real-time demo
    Integrate matlab with Raspberry Pi or port algorithm to Python
Notes: EMILY

## Slide 14: Questions?